## Slide 1: From 3G to 6G
Etienne SICARD
Professor INSA University of Toulouse, France

## Slide 2: Reference
5ÈME INNOVATIVE SMART SYSTEMS
  I5SSCM11 – COMMUNICATIONS - Resp D.Dragomirescu
  COURS : PROTOCOLES POUR LES OBJETS CONNECTÉS
  S. Abdellatif / D. Dragomirescu / E. Sicard
  PART : FROM 3G TO 6G
  2 slots + 3 presentation slots (Students not following IoT Valley or TBS)
  https://moodle.insa-toulouse.fr/course/view.php?id=979
5ÈME ANNÉE AUTOMATIQUE ELECTRONIQUE
  EMBEDDED SMART POWER ELECTRONICS (ESPE)
  I5AELA11 - Logiciel et automatique embarquée pour l'énergie – Resp. G. Garcia Programmation faible énergie pour l’IOT – A. Boyer
  Part : FROM 3G TO 6G : E. Sicard
  3 créneaux cours + 2 créneaux de présentations orale (11 étudiants)
  https://moodle.insa-toulouse.fr/course/view.php?id=776

## Slide 3: Subjects
I5SSCM11 : Oral presentation
  Oct. 13,20
I5AELA11 : Oral presentation
  Nov. 10,21
Send your subject & contributors to Etienne.Sicard@insa-Toulouse.fr list of 1-2 speakers
5G: developing countries
5G modulations
5G infrastructure
mobile Health & 5G
Iridium Next, OneWeb, Starlink, Kuiper
NB-IoT, LoRa & Sigfox
LTE-M for IoT
Drone-trains
5G: Vehicule to Vehicule
5G: Vehicule to EveryThing
Cancer & EM waves
Mm waves threats
Mobile addictions
Vision of ITU
6G modulations
6G antennas
Anti-5G/6G
Technologies for 6G
Nokia & 6G
Ericsson & 6G
Apple & 6G
Samsung & 6G
Orange and 6G
Environmental issues 5-6G

## Slide 4: Evaluation
What students should prepare
Oral presentations
English Français
5ESPE: 1 or 2 students, 15 mn + 5 mn questions
5ISS : 2 students : 10-15 mn+5 mn questions
Evaluation based on
Quality of presentation
Within the time frame
Review, state of the art
Clarity of introduction, figures, conclusion
Synthesis effort
Citation of sources of documents and figures
Personal opinion on the subject area
Opening up to other areas or future technologies

## Slide 5: Web sites
http://fr.wikipedia.org/wiki/5G
https://www.cartoradio.fr

## Slide 6: Reference reports
https://www.ericsson.com/en/mobility-report
http://www.3gpp.org
LTE releases (3,4,5,6 G)

## Slide 7: Reference reports
Scholar.google.fr

## Slide 8: CONTENTS
CONTENTS
Page 01
Technology scale down
Stories about mobiles
Introducing UHF
Modulations for mobiles
3G
4G
5G
Future

## Slide 9: PART 1
TECHNOLOGY SCALE DOWN

## Slide 10: THE ELECTRONIC MARKET GROWTH
83
86
89
92
95
98
01
04
-10%
0
10%
Year
07
20%
PC in companies
Audio CD
Defense
Companies
10
30%
13
16
Individuals
Society
PC at home
Internet
GSM
MP3
DVD
Flat screens
Automotive
Renewable Energy
Security
Medical
Telecom crash
Bank crash
HDTV
3G
4G
IoT, 4K
ADAS
Recession
Recession
4%
2017
Consumer Electronics Market Growth
19
22
25
6%
2024
5G
8K
DCAI
Smart home
Cloud
CoVid
4%
2020

## Slide 11: Context
VISION 2023-2030
Increasing disposable income,
Expanding urban population,
Growing internet penetration and
Availability of strong distribution network
Cloud and virtualization
The electronics market is expected to reach 2 T$ in 2030 at a CAGR of 6%
0
5%
10%
Smartphones
TV
Game consoles
Medical
IoT
Laptops
Servers
Automotive
Growth 2023-2030
0.6
15%
0.3
0.2
0.4
0.3
0.1
0.2
0.1
Electronic Sales 2030 (T$)

## Slide 12: Context
SIX YEARS AGEO… (OCT. 2016)
5 billion subscribers, do you hear me?
https://www.gsmaintelligence.com/data/

## Slide 13: Mobile phones
3G+
4G
4G+
10k
100k
1M
1996
2000
2002
1998
2004
GSM
14k
GPRS
64k
Year
2006
Bandwidth (bit/s)
2008
10M
100M
Average bandwidth
HSDPA
1.0 M
HSUPA
4 M
2010
LTE
20 M
UMTS
120 k
Boundaries
2G
3G
2012
LTE-A
40 M
2014
2020
5G
IMT 2020
100 M
1G
6G
10G
2030
1 G

## Slide 14: 3GPP
6G
3G
5G
4G
3GPP
Rel-4
NGN
Rel-99
UMTS
IMT 2000
Rel-5
HDPA
DL
Rel-8
LTE
Rel-6
HSPA
UL
Rel- 7
HSPA+
Rel-9
LTE
improved
Rel-11
LTE-A
improved
Rel-10
LTE
Advanced
IMT
Advanced
Rel-12
Proximity
Services
Rel-14
5G Phase 1
IMT
2020
Rel-13
LTE
Advanced
Pro
Rel-15
Rel-16
5G
Phase 2
LTE-AP
improved
2000
2010
2020
Rel-17
5G
Phase 3
Rel-18
5G+
Rel-19
Rel-20
Rel-21
2025
Rel-22
2030
6G Phase 1
6G Phase 2
6G+
Rel-23

## Slide 15: TECHNOLOGY TRENDS
Technology
Complexity
2000
130nm
Embedded blocks
2005
90nm
250M
Core DSPs
10 Mb Mem
2010
45nm
500M
Dual core
Dual DSP
RF
Graphic Process.
100 Mb Mem
Sensors
2015
28nm
2G
Quad Core
Quad DSP
Image Proc
Crypto processor
Reconf FPGA,
Multi RF
1 Gb Memories
Multi-sensors
7G
Mobile generation
3G
3G+
4G
5nm
150 G
2020
5G
14nm
4G+
Today
Octa Core
Multi DSP
3D 4K
4 GPU
Crypto, sensor, position processor
Agregated RF
2 Gb Memories
15G
Same +
8K Image
+ 4/8 cameras
+ 16 GPU
+ dual IA
+ MIMO
+ 27 GHz band
2030
6G
15A
1 T
+ More IA
+ Cm localization
+ Zero En. Dev.
+ Ext. MIMO
+ 100 GHz band

## Slide 16: Scale down benefits
65nm
14nm
5nm
65nm
14nm
5nm
..
…
…

## Slide 17: Context
Technology node (nm)
Intrinsic perf.
Strain
Gate material
FinFET for increasing drive current and reducing leakage
MOS
Current drive (mA/µm)
2.0
1.0
0.0
1.5
0.5
Strain to increase mobility
High K Metal Gate to increase field effect
Ioff: 100nA/µm
High performance
10nA
1 nA
General Purpose
MOSFET
130
45
65
90
10
20
32
14
7
5
2.5
FINFET
Nano-Sheet FET
3
20A
18A
15A
Complementary FET
NSFET
CFET
Low power

## Slide 18: Technological trends
Gate
Source
Drain
Gate
Source
Drain
Gate
Source
MOS FET
Fin FET
Nano-Sheet FET
Fin
Nano-sheet
W
W
Drain
MOS
FinFET
NanoSheet FET
More current in the same space
Much more current in the same space

## Slide 19: Technology trends
Device technology innovation – in short
90
nm
180
nm
45
nm
22
nm
FinFET
High K dielectrics
Strain
MOS options
14
nm
Super
FinFET
3
nm
Nano-Sheet FET
20
A
Buried Power Layer
15
A
Stacked N&P
10
A
Stacked tiers

## Slide 20: TECHNOLOGY TRENDS
Qualcomm Snapdragon 888 5G & AI
Silicon lattice: ___ nm
Samsung Exynos 1080 – 5G & AI

## Slide 21: TECHNOLOGY INNOVATION & COST
Chart: Fab cost (Million $)
| 130nm | 90nm | 65nm | 45nm | 28nm | 20nm | 14nm | 7nm
Fab cost | 1450 | 2000 | 2500 | 4000 | 4850 | 6200 | 6700 | 7300
Chart: Design cost (Million $)
| 130nm | 90nm | 65nm | 45nm | 28nm | 20nm | 14nm | 7nm
Design cost | 15 | 24 | 34 | 60 | 100 | 140 | 190 | 270

## Slide 22: Technological trends
2020
2021
2021
Spending billions..
2022

## Slide 23: PART 2
STORIES ABOUT MOBILES

## Slide 24: HISTORY OF MOBILE COMMUNICATIONS
1940: 1st wireless telephone invented by Bell System
1978: 1st analog cellular network AMPS in Chicago (1G)
1981 : 1st digital cellular network RITA
1985: 1st analog french cellular network, Radiocom 2000
1993 : GSM network started in Europe (2G)
1996 : DCS 1800 network started in Europe
2001 : IMT 2000 – UMTS (3G)
2005 : France starts 3G
2008 : France starts 3G+
2010 : Teliasonera starts LTE in Sweden (notebooks)
2011 : Bouygues, Free Orange, SFR on 4G
2012 : LTE worldwide (4G)
2014 : LTE-Advanced worldwide (4G+)
2018 : IMT 2020 (5G) started in South Korea & USA
2019 : First 5G mobiles
2020 : 5G – Olympic Games – Japan
2025 : 5G+
2030 : 6G
1G
2G
3G
4G
5G

## Slide 25: MY COURSE IN 2001
I started to teach “GSM” in 1999
Forecast: 1,000,000,000 subscribers in 2003
.. And then, the “Telecom crash” in 2000

## Slide 26: IRIDIUM
$7 billion
Motorola design: 77 satellites on 7 orbital planes, 11 satellites at 33 degrees
4000 km between each satellite
Iridium = atomic number 77
Final constellation: 66 satellites (Iridium still used…)
Low-orbit satellites (780 to 800 km)
$7 billion constellation
Misjudged competition and mispredicted technology
Poor marketing; service far too costly
$5 billion bankrupt in 2000
Iridium Satellite, paid $25m saving its network of satellites from being sent out of orbit to burn up
Kosmos 2251 crashed into Iridium 33 in 2009 (Video)

## Slide 27: IRIDIUM NEXT - $3 billion
June 2, 2010 Iridium Next announced in 2016 with Thales Alenia Space, ($2.9 billion) and SpaceX (2015)
"We are excited to be Iridium's lead supplier in the design and build-out of the Iridium NEXT constellation," said Reynald Seznec, CEO of Thales Alenia Space.
Iridium Next fleet has 75 satellites (2020)
75 satellites + 9 on orbit + 6 on earth

## Slide 28: OneWeb – $50 Billion
Bridge the digital divide by 2027
Half of world population has no internet access
Affordable Internet access for everyone
Connect every school on Earth
600 satellites for “Space Internet”
Initial date: 2025
7 terabits per second capacity
Bankrupt March 2020
Launched 75 satellites end 2020
16 Ariane launches x 35 satt.
Sold 1B$ to U.K. Gov. and Indian telecom. Bharti Global
http://www.oneweb.world

## Slide 29: FREESCALE TOULOUSE
“Freescale is shaping up to be one of the ugliest buyouts in history” (2008, Bloomberg Business Week)
On Mar. 26, 2008, Motorola announced it was spinning off its cell-phone unit
In Toulouse, 250 persons from CPG were fired
SigFox, Beenetic, MHComm start-ups created
NXP and Freescale merged
Qualcomm willing to merge with NXP

## Slide 30: Autonomous drive
TOWARDS AUTOMATIC DRIVE
2020 : Injury-free driving
2030: Accident-free driving ?
2040: Autonomous driving?

## Slide 31: Autonomous trains
Continental Holistic Connectivity
SNCF Astom Bombardier autonomous TER
“Drone Trains”

## Slide 32: Autonomous drive
PSA Feline
VALEO Xtra Vue

## Slide 33: Mobile subscriptions
Mobile Business
https://www.ericsson.com/en/reports-and-papers/mobility-report

## Slide 34: MOBILE TRAFFIC
https://www.ericsson.com/en/reports-and-papers/mobility-report
1 Tera
1 Exa
1 Peta
1 Giga
1 Meg
1 K
10
3
10
9
10
6
10
12
10
18
10
15
1 Zetta
10
21
1 Yotta
10
24
+50% per year
We are here
120 Exa Byte per month
CoVid: Subscribers’ average usage during the 9 am-to-5 pm daypart has risen to 6.3 GB, 41.4% higher than the January figure of 4.4 GB.

## Slide 35: MORE RESOLUTION THAN TV
4K
UHD
3840
2560
1920
1280
720
1080
1440
2160
2K WQHD
FHD
HD
UHD = Ultra High Definition
WQHD = Full High Definition
UHD = Ultra High Definition
SUHD = Super Ultra High Definition
4K TV
7680
8K
SUHD

## Slide 36: TOWARDS AN INCREASED EFFICIENCY
Mobile
3G
8 U
3G+
10-15 U
4G
15-40 U
WiFi
100 U
WiMax
25-50 U
Packet
U= bit/s/km2/Hz
5G
100 U
6G
500 U

## Slide 37: MOBILE GENERATIONS
Technico-economical
analysis
Submit a business plan
Buy license
Invest
Deploy the network
Install, setup
Launch network, infrastucture
Optimize, extend, densify
Start exploitation
Service Evolution
New needs, new plans
Stablilization, growth, ROI
Transition to a new technology
From S. Tabbane, Ing Réseaux Cellulaires, Hermes, 2002
5 years

## Slide 38
2003
2006
2009
2012
Year
Pioneers
Visionneers
Immaturity
Soccer World Cup
Pragmatism
Late majority
Latest
2015
2018
Your teacher
4G Customers
4G Pioneers
2021
3G TO 5G
We are here
3G Customers
5G Customers
2024
35%
MOBILE GENERATIONS
Pioneers

## Slide 39: PART 3
INTRODUCING ULTRA-HIGH FREQUENCIES

## Slide 40: BANDWITH
TNT
470
700
4G
800
2-3G
900
1 GHz
2-4G
1 800
3G
1 900
2 GHz
4G
2 600
3 GHz
5G
3 400
5G
700
5G
26 000
6G (D)
92 000
114 000
https://fr.wikipedia.org/wiki/5G
Medium
cells
Large cells
Small cells
Low data rate
High data rate
Medium
Data rate
25 GHz
100 GHz
6G (W)
130 000
174 000

## Slide 41: BANDWIDTH
GSM (2G)
DCS 1800 (2G/4G)
890
915
935
960
f(MHz)
1710
1785
1805
1880
f(MHz)
E-GSM
880
925
UMTS (3G)
1920
1980
60
2110
2170
4G, 4G+
2500
2570
2620
2690
70
f(MHz)
f(MHz)
771
821
30
832
862
25
5G
470
3800
TNT
f(MHz)
703
45
5G (2023)
748
400
3400
75
1000
26 500
27 500
758
788

## Slide 42: Frequency spectrum
Giant number of communication systems upto 275 GHz
FM 88-108 MHz
TV 174-216 MHz
Empty: 275-300 GHz
5G 27 GHz

## Slide 43: Frequency spectrum
Vision of SAMSUNG : 6G Spectrum - Expanding the Frontier
W-band (92-114.25 GHz), D-band (130-174.8 GHz), 220-275 GHz
O2

## Slide 44: Operators
Example of 4G band in France: 3-4 operators
4G
800
https://fr.wikipedia.org/wiki/LTE
4G
2600
2-4G
1800

## Slide 45: 5G IN FRANCE
Prix de licence: 1,5 Md€

## Slide 46: FREQUENCY SCAN
2-4G
1800
3G
1900
3G
2100

## Slide 47: [S] MEASUREMENTS
DESIGN CONSIDERATIONS FOR INTEGRATED MOBILE PHONE ANTENNAS
D. Manteuffel, A. Bahr, D. Heberling, I. Wolff, ICAP 2001
DCS 1800MHz
S11 (reflected power)
Antenna Design Example

## Slide 48: FORMULATIONS
4G: 2600 MHz
/… = __ cm
c= 3e8 m/s,
f = frequency in Hz
 = wavelength in m
IPHONE 4
5G: 25 GHz
/… = __ cm

## Slide 49: ANTENNA ARRAYS
Millimeter spectrum has room for “Gbps/per user”
Beam forming is done by antenna arrays
5G: 28 000 MHz
= __ mm
/2 = __ mm
Ojaroudiparchin, N.. A 28 GHz FR-4 compatible phased array antenna for 5G mobile phone applications. In Antennas and Propagation (ISAP), 2015 International Symposium (pp. 1-4). IEEE.

## Slide 50: BANDWIDTH DEFINITION
3 MHz
/4 25 m
30 MHz
/4 2.5 m
300 MHz
/4= 25 cm
3 GHz
/4= 2.5 cm
30 GHz
/4= 2.5 mm
HF
VHF
UHF
SHF
xHF
300 GHz
/4= 250 µm
THF
Infra red
Visible (0.7µm)
Mobile
WLAN
1G
2G
4G
8G
12G
25G
L S C X Ku K Ka
3 THz
/4= 25 µm
microWave
mmWave

## Slide 51: RF SENSITIVITY
dB = 20 log10 Vout/Vin
dBV = “decibel volt ” = 20 log10 V
1µV = 10-6V
In RF
Formulation
V (dBµV) = 20 log10V +___
Exercise
dBµV
V
1
100m
10m
1m
100µ
10µ
1µ
100n
10n

## Slide 52: RF POWER
dBm = “decibel milliwatt ” = 10 log10 (P* 103)
Power unit
Warning
dBm
W
1000
100
10
1
100m
10mW
1mW
100µ
10µ
1 Watt = ____mW = __ dBm
0dBm on 50  = ____ dBµV
Exercises

## Slide 53: ANTENNAS

## Slide 54: ANTENNAS
eNodeB Sofia Antipolis
https://lafibre.info > 4g
BTS & Node B antenna placed on one of the Churches in Sopot, Poland

## Slide 55: BASE STATION EVOLUTION
https://fr.slideshare.net/KarvaCarbi/antenna-evolution-from-4g-to-5g-70581361

## Slide 56: ANTENNAS
20.0
40.0
60.0
Radiation resistance
Ground plane area
Quater-wave monopole

## Slide 57: ANTI-5G

## Slide 58: EFFECT OF WAVES
UMTS 1.9 GHz
Micro-wave: 2.45GHz
© encarta
Main effect at 2 GHz : heat
OVERVIEW

## Slide 59: Fields
Maximum field: 20 V/m
  Average field 5 V/m.
  Experts ask 0,6 V/m to limit biological impact
Doctors suggest to not use mobile phones before 16 years old.
10-20 V/m during communications
  TGV. Close to engines: 300 V/m.
  Iron. 120 V/m.
  Television. 60 V/m.

## Slide 60: HEALTH EFFECTS
OVERVIEW
« Improved auditory memory talk with EM field emitted by cellular phones »
C.M Krause, C. Haarala, L. Sillanmaki, Bioelectromagnetics, vol 25, pp 33-40, 2004
Overheat 0.5°C : acceleration of nerve influx propagation
http://www.cancerresearchuk.org

## Slide 61: Smartphone addiction
No Mobile Phobia (nomophobia)
Smartphone addiction 40% of teens in India
45% of addicts: headache, trouble concentrating, memory loss, hearing loss, fatigue…
Damage interpersonal skills, negative health risks and harmful psychological effects

## Slide 62: Risks
More than half of all trips that ended in a crash also included some form of distraction from a mobile phone.
1rst cause of death on European roads (20%)
« Dead by smartphone »
National Highway Traffic Safety Administration / The New York Times

## Slide 63: Against 5G
« Continuer à promouvoir des technologies superflues et énergivores comme la 5G ou la voiture autonome est irresponsable à l’heure où nos modes de vie doivent évoluer vers plus de frugalité et où nos efforts collectifs doivent être concentrés sur la transition écologique et sociale. » Tribune initiée par :
Joana Beigbeder, Frédéric Boone, Milan Bouchet-Valat, Julian Carrey, Agnès Ducharne, Tanguy Fardet, Kévin Jean, Jérôme Mariette, Françoise Roques,

## Slide 64: MOBILE PHONE PROPAGATION
Reflection
Screening
Diffusion
Diffraction
Orange labs Belfort – REE Feb. 2010
Jean-Marc CONRAT « Utilisation des photos panoramiques pour la compréhension des phénomènes physiques du canal de propagation »
OVERVIEW

## Slide 65: ATTENUATION
d
Attenuation (dB) =32+30 log(f)+20 log(d)
f in MHz
d in km
Urban UMTS:
Attenuation (dB)=133+34 log(d)
d en km
OVERVIEW

## Slide 66: PART 4
Roadmap to 6G

## Slide 67: Roadmap to 6G
Vision of NOKIA

## Slide 68: Roadmap to 6G
Vision of NOKIA - Spectrum for 6G explained

## Slide 69: Roadmap to 6G
Vision of HUAWEI

## Slide 70: Roadmap to 6G
Use case according to HUAWEI

## Slide 71: Roadmap to 6G
Orange’s vision for 6G - White paper 2022
Introducing Zero-Energy Device (ZED)
Sub 6GHz
100-300 GHz

## Slide 72: Roadmap to 6G
Banafaa, M., (2023). 6G mobile communication technology. Alexandria Engineering Journal, 64, 245-274
Alraih, S., (2022). Revolution or evolution? Technical requirements and considerations towards 6G mobile communications. Sensors, 22(3), 762.

## Slide 73: 6G
Ericsson White Paper 2022 « 6G - Connecting a cyber-physical World”

## Slide 74: 6G
5G advanced in 2025
6G in 2030
Ericsson White Paper 2022 « 6G - Connecting a cyber-physical World”

## Slide 75: Roadmap to 6G
Banafaa, M., (2023). 6G mobile communication technology. Alexandria Engineering Journal, 64, 245-274.

## Slide 76: Roadmap to 6G
Banafaa, M., (2023). 6G mobile communication technology. Alexandria Engineering Journal, 64, 245-274.

## Slide 77: Roadmap to 6G

## Slide 78: Thank you for your attention
Etienne.sicard@insa-toulouse.fr